Installation Instructions

The Tuscany

(NOTE: Thin cast stone mantels are produced with a texture and color that replicate the appearance of natural stone. Due to the natural characteristics of the material and manufacturing process, variations in color shade and surface texture are normal. We do NOT recommend that gypsum based fireplace mantels be placed next to ventless or direct vent fireplaces without a hood and a circulating fan. Failure to do this will void the warranty.)

Construction adhesive will be needed to mount your surround. Use one that works for the types of materials you will be bonding to. You will also need a screw gun to mount the product.

New Package: Each surround is packaged in its own crate.

Before unpacking: Carefully remove each piece from the package without scratching the exterior finish.

Always carry or transport the header and hearth vertically and not flat like a table. We don't want to put too much stress on these long pieces and possibly cause cracks.

START WITH THE HEARTH

Prepare the surface to receive the hearth. The hearth can set on the sub-floor or hardwood flooring but not on carpet or easily combustible material. Make sure the floor is clean and has nothing sticking up that would not let the hearth set flush on the floor. You can use a mastic or construction adhesive to set the hearth. Keep it away from the edges of the hearth so it won’t squeeze out from under the hearth.

Set the hearth and center it on the firebox so that the entire mantel will be centered around the fireplace.

INSTALL THE LEGS

Put adhesive on the back of one of the surround legs. There is a left and a right leg. Set one leg at a time. The bottom of each leg has a tab the matches up with the hearth. Align leg tab into hearth and push leg against the wall. Repeat on the other leg. Measure 59-1/2” from outside of left leg to the outside of right leg. Use 1-5/8” screws to secure Leg L-Brackets to wall.

INSTALL THE HEADER SHELF

Dry fit the Header Shelf. Set Header Shelf on Legs carefully. The top of the legs have lego type blocks to go into recesses in the bottom of the Header Shelf.

Be careful not to drop the Header Shelf on the Legs or force the fit. Ease it in place and hold it there. Have someone mark with a pencil where the top of the shelf is on the wall. Do this where the two studs on either side are located.

Remove the shelf –Carefully!--

Measure the thickness of the top of the shelf, on the back side. This will tell you where to mount the 2” X 2” mounting strip (included) will be screwed to the wall. If you do this correctly your shelf will sit square on top of the header.  Screw the mounting strip to the wall, into the studs with some adhesive behind the strip to hold it more securely to the wall. Dry fit your Header Shelf again to make sure it lines up correctly. Don’t let it go, hold on! If it works, take it down.

Now put construction adhesive on top of the mounting strip and around the back perimeter of the Header Shelf. Make sure you keep it away from the finished outside edge so that it won’t squeeze out and be seen.

Set Header Shelf on Legs carefully.

Push Header Shelf firmly against the wall and secure to the mounting strip through the pre-drilled holes in the top of the shelf using the 3” screws .

When securing the shelf in place make sure you don’t over tighten or the shelf may crack!

# Text boxes

Measure center of firebox

Apply adhesive to hearth

Flip and Center hearth on firebox

Measure legs and adjust to 59-1/2” (+0”/

-1/16”) from outside of leg to outside of leg measured at the very top of the legs. This dimension is critical to the Header Shelf  meeting up with the legs. Make sure the bottom of the legs are still flush against hearth.

Apply adhesive

Secure Leg  L-Brackets to wall using 1-5/8”.  Double check the 59-1/2” dimension

screws.

Dry fit shelf and mark the top of the shelf

Place another mark below the top mark the thickness of the top

Screw mounting strip to the wall into the studs

Apply adhesive to the top of the mounting strip

Secure Header Shelf to mount block using 3” screws.

Apply construction adhesive surface and inside of tab recess on the left and right hearths. Flip place and push against center hearth.